## Slide 1: Control setup for BVTs
REST CLIENT
REST
REST SERVER
MATLAB
DSP Tx
DSP Rx
AGENT CORE
LASER iface class
NETCONF SERVER
MZM1
DAC1
ADC1
BVT1 Agent
TLS1
REST CLIENT
AGENT CORE
LASER iface class
NETCONF SERVER
BVT2 Agent
MZM2
DAC2
ADC2
TLS2
SDN controller
BVT1
BVT2

## Slide 2: Hardware details
TLS1: YENISTA OSICS ch 2
TLS2: YENISTA OSICS ch 3
DAC1: LEIA DAC HI channel; ‘dac_out=1’
DAC2: LEIA DAC HQ channel; ‘dac_out=2’
ADC1: Tek DPO 70000C ch1; ‘osc_in=2’
ADC2: Tek DPO 70000C ch4; ‘osc_in=1’
MZM1: Photline MX-AN + Photline DR-AN driver
MZM2: SumiCem + SHF-807C driver

## Slide 3: DRoF agent and data model (YANG/NETCONF)

## Slide 4: Workflow

## Slide 5: Workflow actions per agent
Agent 1: NETCONF rpc <edit-config> create [constellation, equalization, NCF, FEC]
  Laser setup
    Ensure laser off: laser.enable(ch, False)
    Calculate lambda0 from NCF -> use exact value for c=299792458 m/s
    Set laser wavelength: laser.wavelength( ch, lambda0)
    Set power to max (14.5 dBm): laser. power(ch, 14.5)
    Set laser on: laser.enable(ch, True)
  DAC setup
    From constellation, extract Bn and En
    Generate waveform and load to DAC channel: @REST dac.transmitter(dac_out, Bn, En)
    Store Bn, En, equalization and FEC for Rx monitoring!
Agent 1: NETCONF rpc-reply OK
Agent 2: NETCONF rpc <edit-config> create [constellation, equalization, NCF, FEC]
Agent 2: NETCONF rpc-reply OK

## Slide 6: Workflow actions per agent (cont.)
Agent 1: NETCONF rpc get [SNR per subcarrier]
  Receive associated signal: @REST osc.receiver(dac_out, osc_in, bn, En, eq)
  Retrieve SNR per subcarrier from output of @REST osc.receiver()
Agent 1: NETCONF rpc-reply [Measured SNR per subcarrier]
Agent 1: NETCONF rpc <edit-config> (replace) [constellation]
  DAC setup
    From constellation, extract Bn and En
    Generate waveform and load to DAC channel: @REST dac.transmitter(dac_out, Bn, En)
  Update stored Bn and En
Agent 1: NETCONF rpc-reply OK
Agent 2: NETCONF rpc get [SNR per subcarrier]
Agent 2: NETCONF rpc-reply [Measured SNR per subcarrier]
Agent 2: NETCONF rpc <edit-config> (replace) [constellation]
Agent 2: NETCONF rpc-reply OK

## Slide 7: Dataset
Bn1: array Ncarriers, ‘2’
Bn2: array Ncarriers, ‘1’
En1: array Ncarriers, ‘1’
En2: array Ncarriers, ‘1/sqrt(2)’=0.707
Eq1=Eq2: ‘MMSE’
NCF1: 1550.12 nm // 193.4E6 MHz
NCF2: 1550.92 nm // 193.5E6 MHz
FEC1=FEC2: ‘HD-FEC’